## Slide 1: PyTorch-to-FPGA for QNNs with
@ ONNX Community Virtual Meetup, 2020-04-09
Yaman Umuroglu
Xilinx Research Labs

## Slide 2: Xilinx Research, Dublin
Established over 14 years ago
  Slowly expanding and increasingly leveraging external funding (IDA, H2020)
  6 full-time researchers + interns
Applications & Architectures
  Quantifying the value proposition of Xilinx devices in machine learning
In collaboration with Partners, Customers and Universities
Lucian Petrica, Giulio Gambardella, Alessandro Pappalardo,
Ken O’Brien, Michaela Blott (leader), Nick Fraser, me (from left to right)

## Slide 3: Exploring Custom Hardware + Algorithms for DNNs
dog
cat
cat
dog
FPGA
CNN
allocated resource ~ compute requirement
per layer
sum
+2
-4
+1
act.
* +1
* -1
* -1
+1
k-bit weights and activations, k <= 4
keep all on-chip!
Notes: Default approach in FINN
Explain what’s going on in the animation, and then play animation (same with the slide before)
Customize both the precision and the structure of the compute engine
Compute engine structure mimics the NN in hardware, all layers process in parallel, in pipeline fashion (animation)

## Slide 4: Few-bit QNNs + FPGA Dataflow: Showcases
ResNet-50 on Alveo U250
2 ms latency
2000 FPS
Complex
Topologies
High Throughput
& Low Latency
MNIST MLP on ZC706
12.3 M FPS
310 ns latency
Low-Power, Real-Time
Object Detection
Tincy-YOLO on Ultra96
55 FPS @ 10 W
Notes: Work on FINN has resulted in a number of technology demonstrators which validate approach at various scales
Multi-layer perceptron acceleration, MNIST but also consider other applications such as high-energy physics
Object detection and clasiffication, relevant to ADAS applications
Object clasiffication for data-center applications

## Slide 5: The FINN Project: Mission
End-to-end flow to lower adoption barrier
Codesign
Support hardware architecture exploration around dataflow execution
Support customizing the algorithms with precision, layer types, topologies
Open source from the ground-up to encourage community contributions
Transparency and flexibility through open source (if not supported, add your own!)
Flexibility
on
Algorithms
Flexibility
on
Architectures
Notes: Key challenge – how do we realize conversion from full precision network to dataflow implementation in FPGA, through codesign;
FINN vision: Enables customization at the neural network level and FPGA accelerator level
Designed as enabler towards FPGA inference for a wider audience
user not customer

## Slide 6: The FINN Project: Components of the Stack From PyTorch to FPGA
QNN training in PyTorch
Brevitas
Frontends, Transformation, Dataflow Backend
FINN Compiler
Deployment with
Customization
of Algorithm
Customization
of Hardware
Architecture
Notes: How we plan to accomplish this mission: stack of modular components
Brevitas provides algorithmic customization, FINN compiler generates hardware accelerators
Designed for easy integration with Pynq, although other runtimes exist

## Slide 7: An Overview of the FINN Compiler
Python library of graph transformations
  Each consumes and produces an ONNX graph
User calls sequence of transformations to create their own flow
  Example end-to-end flows to get started
Primary backend target is our own Vivado HLS library
  Templated datatypes, configurable parallelism
Code Generator
Import
FINN HLS Library
Synthesizable description
Hardware Cost Model
Vivado
Synthesis, PAR
Software Library
Host Run-time
FPGA Platform
ONNX
Streamlining
Hardware Mapping
Resource Allocation

## Slide 8: How We Use ONNX in the FINN Compiler
Custom quantization annotations
for few-bit types
Use quantization_annotation
ONNX float32 tensor as container,
values restricted to few-bit types
indicated by type name (string)
Hybrid runtime to
verify model correctness
Mix onnxruntime, Vivado HLS
C++ and RTL (PyVerilator)
Not performance-oriented
Custom op_types
at different abstraction levels
Identified by op_type and domain
Python wrappers to provide
implementations for exec, codegen..

## Slide 9: How We Use ONNX in the FINN Compiler
Library of Python
graph transformations
Operating directly on ONNX
representation
Including constant folding, shape
inference, convolution lowering ++
Tensors with custom
data layout and packing
e.g. pack 8x1-bit as 1x8-bit
Utility functions to convert back
and forth
Use Netron for debugging
Visually inspect transformed graphs
Check node attributes, initializers

## Slide 10: Join our Growing Open-Source Community!
Japanese documentation effort + «cucumber sorting»
University courses, student/hobbyist projects
Sketch Recognition (Xilinx Edinburgh)